## Slide 1
INTERNAL BRIEFING · SAAB / KTH
Joint emitter and mode clustering from mixed PDW streams
What the data looks like, how the encoder works, and which scores actually moved.
Problem · Data · Encoder · RoPE / bias · Takeaways
Markus Johnson Swegmark Supervisors: Alexander Karlsson, Elin Ohlman (Saab) · Saikat Chatterjee (KTH)
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
1 / 15
Notes: Internal walkthrough, not a defence. Data and the two attention tricks first.

## Slide 2
One mixed stream, two partitions
Emitter · deinterleaving
IDs unique only inside this recording.
Unknown how many platforms are present.
We recover a partition, not a name.
Mode · operating schedule
19-type catalogue, shared across recordings.
Same mode can sit on several emitters.
Inference still clusters — no catalogue softmax.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
2 / 15
Notes: Classical chain deinterleaves first. We want both partitions from the mixed list.

## Slide 3
Three questions
RQ1
Can a transformer deinterleave pulses and recover modes by clustering a window of PDWs?
RQ2
Does training both jobs together beat training deinterleaving alone?
RQ3
Does a pairwise physical bias, or rotary encoding of pulse coordinates, actually help?
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
3 / 15
Notes: Answers at the end. First the data.

## Slide 4
Dense lock-on versus sparse scan
L = 2000
pulses / window
1 169
test windows
~3 / ~6
emitters / modes
19
mode types
Orange: lock-on, low PRI, fills the window.
Purple: scanning. Only seen when the beam sweeps the receiver.
Amplitude is the giveaway — lobes, not a line.
Scan period 2–5 s, so one window may contain a single lobe.
A density clusterer on RF/PW ignores the sparse class.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
4 / 15
Notes: Walk the amplitude panel. Gaps between purple lobes are the rotation.

## Slide 5
Slow scans and lock-on floods
Left: one scanning mode. Incidence drifts; amplitude follows the beam. Density methods oversplit a smear.
Right: 3 pulses vs 1997 in the same window. One lock-on, one long PRI or mid-scan. A 3-pulse train is a poor later mode input.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
5 / 15
Notes: Feature DBSCAN completeness 0.52 on emitters: extra clusters that are internally pure.

## Slide 6
Crowded mixtures: RF and PW are not unique IDs
Several platforms share frequency and pulse-width bands.
Lock-on (flat) sits next to scan (curves).
Timing structure is the remaining cue.
This is the Vanilla emitter tail: about one window in ten.
All-pairs attention is the bet: sparse trains have to find each other across a flood.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
6 / 15
Notes: Why attention rather than an O(L) state.

## Slide 7
L pulses in, L embeddings out
Self-attention: every pulse scores every other pulse. That mix is deinterleaving.
Cost is O(L²), so we window at L = 2000 rather than the whole recording.
LSTM is O(L), but a hidden state has to carry a 3-pulse train across a lock-on flood.
Mamba / SSMs compress the past into a state. Pairwise “same PRI train?” is a comparison, not a state update.
We did not bake off Mamba. The bet is that paying L² is worth it when the physics is pairwise.
Then DBSCAN on the embeddings. Cluster IDs are local to the window.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
7 / 15
Notes: Do not claim a Mamba bake-off. Claim the inductive bias.

## Slide 8
Shared trunk, two heads, two positive sets
~16 M parameters. Width 256, 8 heads.
Emitter loss: same recording-local ID.
Mode loss: same global catalogue label.
Same contrastive kernel. Only the positive set changes.
Joint training is the unweighted sum.
DBSCAN at inference. Not in the loss.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
8 / 15
Notes: The two similarities can fight in the trunk.

## Slide 9
Two ways to put physics into attention
RoPE-TOA
Rotate Q and K by window-local ToA.
The score is a dot product, so the enclosed angle matters.
Only the relative rotation R(Δt) enters the product.
No extra weights. Encoder ~2.5 ms.
Physical bias
Build B_ij = |p_i − p_j| from ToA and incidence.
Scale by learned λ, subtract from the attention matrix A.
Same emitter scores as RoPE-TOA.
Encoder ~32 ms. Extra L×L maps in every head.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
9 / 15
Notes: Next two slides are the animations. Let them play once.

## Slide 10
RoPE-TOA · the score is the rotated dot product
q · k = cos φ.
Rotate each by its own ToA.
New angle: φ + Δt · ω.
Close in time → small extra twist, high score.
Far in time → larger twist, lower score.
GIF loops. Prefer the MP4, play once.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
10 / 15
Notes: Vanilla already has ToA as a channel. RoPE puts Δt into every query-key product.

## Slide 11
Physical bias · learned λ on delta maps, subtracted from A
|ΔToA| and |Δ incidence| from the inputs.
λ_t, λ_x: one scalar per head.
Bias λB is subtracted from vanilla A.
Same-direction, nearby pulses stay bright.
Maps are L×L. That is the bill.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
11 / 15
Notes: A cache skips rebuild, not the quadratic subtract. RoPE is the cheap twin.

## Slide 12
Vanilla already works on most windows
Feature DBSCAN emitter ARI 0.58, ~7 extra clusters. Completeness 0.52.
Vanilla joint: 0.95 emitter, 0.99 mode.
88% of windows ≥ 0.99. About 1 in 10 below 0.90. That tail is the story.
RoPE-TOA and Bias stay down until just below 1. None below 0.90.
Stacking them is worse than Vanilla (57% vs 88% at ≥ 0.99).
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
12 / 15
Notes: RQ1 is yes, with a leftover deinterleaving tail. Mode is already easier in the raw PDWs.

## Slide 13
Joint is a tax on Vanilla. Time in attention removes it.
Left: emitter-only Vanilla hits 0.999; joint drops to 0.948. Modes do not pay. Right: RoPE-TOA and Bias close the tail (ARI 1.000). An emitter-only RoPE-TOA copy matches joint RoPE-TOA — the tax is a Vanilla problem. RoPE-az 0.973. Stacking the two time devices scores below Vanilla.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
13 / 15
Notes: RQ2 is no for deinterleaving alone. RQ3 is yes for time, no for stacking.

## Slide 14
Same scores, different bills — and what to do with that
RoPE-TOA: +0.9 ms vs Vanilla. Same parameter count.
Bias: ~32 ms encoder. DBSCAN ~55 ms dominates Vanilla and RoPE.
Both partitions from the mixed window → joint RoPE-TOA. Do not stack the bias.
Deinterleaving only → emitter-only Vanilla is already at the ceiling.
Cluster IDs die at the window edge. Tracks need a later association.
Synthetic. Held-out modulations and operational data are not scored.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
14 / 15
Notes: Do not recommend Bias for production on this evidence.

## Slide 15
In one breath
RQ1
Yes. Vanilla recovers both partitions on most windows. Feature DBSCAN does not.
RQ2
No, if you only need deinterleaving. Joint taxes emitters on Vanilla. RoPE-TOA does not pay that tax.
RQ3
Yes for time. RoPE-TOA or the pairwise bias close the emitter tail. Stacking them does not. RoPE is the one you want.
The data is unbalanced because physics is: lock-on versus a 2–5 s scan, low PRI versus high PRI. Attention is expensive because associating non-adjacent pulses is an all-pairs question. Putting time into that product closed the last errors.
Internal briefing · Saab · KTH master's thesis · Markus Johnson Swegmark
15 / 15
Notes: Stop. Questions. Mamba: not compared. Real data: not scored. Tracks: future work.